## Slide 1: Colour, resolution, and memory: a brief history of computer graphics

## Slide 2: What are we talking about when we talk about computer graphics?
Basic “ingredients” of a screen image: pixels, resolution, colour

## Slide 3: Pixels
Images are comprised of pixels (picture elements) – these are the smallest units of information in images.
Normally represented as dots, squares, or rectangles
The colour and intensity of a pixel can be varied

## Slide 4: Display resolution
The display resolution of a computer display refers to the number of pixels that can be displayed in each dimension
    Eg, 1024x768 – 1024 pixels per row, 768 per column
The display resolution is limited by the amount of video RAM available

## Slide 5: Colour
Each pixel can vary in colour.
Early graphics systems used palettes – the colour of each pixel was chosen from a palette of 4, 16, 64, or 256 different colours
The number of available colours was limited by the amount of video RAM available.

## Slide 6: CGA (Colour Graphics Adapter)
First graphics card, introduced in 1981
Equipped with 16kB of memory
At one bit/pixel (black and white), we can have 128000 pixels, or a resolution of 640x200
Highest colour depth is 4-bit colour: red, green, blue, “brightness”, giving 2^4=16 colours. The highest resolution that could theoretically be supported by 16kB of memory is 128000/4 pixels, for a resolution of 320x100, but this wasn’t used

## Slide 7: CGA (Colour Graphics Adapter)
In order to get decent resolution, the 16 colours were not used simultaneously
Instead, 4 colours at a time were used at a resolution of 320x200. Choice of palettes: either
  red, green, yellow, black or
  magenta, white, cyan, black

## Slide 8: CGA palette

## Slide 9: EGA (Enhanced Colour Adapter)
Introduced in 1984
Equipped with 64kB of memory
An extension of CGA, where all 16 colours could be used simultaneously to support a screen of 640x200
Allowed the 16 colours to be chosen from a palette of 64 colours

## Slide 10: EGA palette

## Slide 11: VGA (Video Graphics Array)
Introduced in 1987
256 kB of memory available in standard graphics card
Built on EGA’s 64 colours, but allowing them all to be used simultaneously with a resolution of 640x200
Extended EGA colour palette by providing 256 colours, any 16 of which could be used simultaneously in high resolution mode

## Slide 12: VGA (Video Graphics Array)
Resolutions available:
  640x480 in 16 colours
  640x350 in 16 colours
  320x200 in 16 colours
  320x200 in 256 colours

## Slide 13: VGA palette

## Slide 14: SVGA (Super VGA)
Introduced in 1989
Originally referred to a resolution of 800x600 4-bit pixels (235 kB) memory
…Extended to 1024x768 8-bit pixels (2^8=256 colours, 768 kB memory)
…and beyond, as memory became cheaper and cheaper

## Slide 15: SVGA (Super VGA)
The SVGA monitor (like the CGA, EGA, and VGA monitors) used palettes and could only display a certain number of colours at a time

## Slide 16: High Colour
Introduced in 1989, shortly after SVGA
First graphics card not to use palettes
15, 16-bit high colour
16-bit high colour: each pixel is comprised of three component (red, green, or blue) has 64 levels of intensity, allowing for 65,536 possible colours
First graphics card to generate pixels by varying the intensity of each component (R,G,B) rather than referring to a palette or lookup table.

## Slide 17: High Colour
At a resolution of 1024X768, 1.5MB of memory required
32 bit high colour: red, green, blue, and an additional “flag” to control transparency. 4 bytes per pixel, so supporting a screen of resolution 768x1024 required 4x768x1024 bytes = 3 MB.

## Slide 18: True Colour
16,777,216 colours – 256 for each of red, green, blue
Human eye is believed to be able to distinguish among 10 million different colours

## Slide 19: Deep Colour
Common bit depths for Deep Color include 30 bits (1.073 billion colors), 36 bits (68.71 billion colors) and 48 bits (281.5 trillion colors).